## Slide 1
The IOT Based Jacket
Eng. Elie El Arou
Eng. Atieh Atieh

## Slide 2
Introduction
What is the problem
Our Solution!
Requirements
System Design
Functional Decomposition
Components
The hardware and specification
Outline
Hardware Implementation
Circuit and flow chart
Software Implementation
Project Analytics
Cost, Gantt Chart, Risk Assessment, and Conclusion
Flow Charts, Code Snips And application

## Slide 3
INTRODUCTION

## Slide 4
STATISTICS (1)
300,000 HOSPITALIZED
There is 300,000 elderly individuals hospitalized annually due to broken hips
$ 6,000,000,000 COSTS
medical costs for broken hips in the U.S. is six billion dollars per year
ONE IN FOURTH
one in fourth of the elderly population
report falling each year

## Slide 5
33%
33% of elderly individuals do not survive beyond one year after experiencing a hip fracture
31.8%
31.8% of elderly mortality in the US is cause by heart disease
STATISTICS (2)

## Slide 6
WE HAVE THE SOLUTION!

## Slide 7
ELECTROCARDIOGRAM
Monitor live ECG
O2 LEVEL & HEART RATE
Monitor heart rate and oxygen level with 85 to 90% accuracy
TEMPERATURE
Track body and room temperature with 98% accuracy
PROJECT REQUIREMENTS
FALL DETECTION
Track any fall and deploy airbag
WARMING MODULE
Give warmth through heated sheets
INTERFACE
Displayed and send notification on a web and PWA application
01
02
03
04
05
06

## Slide 8
FUNCTIONAL DECOMPOSITION LEVEL 0

## Slide 9
FUNCTIONAL DECOMPOSITION LEVEL 1

## Slide 10
HARDWARE COMPONENTS
ELECTROCARDIOGRAM
AD-8232
FALL DETECTION
MPU-6050
Heating pads
Heating pads
MICROCONTROLLERS
ESP-8266 & ESP-WROOM-32
BLOOD OXYGEN LEVEL
MAX-30100
BODY TEMPERATURE
DS18B20

## Slide 11
ESP-8266
Specifications
Price: 3.5$
Microcontroller: Tensilica 32-bit RISC CPU Xtensa LX106
Operating Voltage: 3.3V
Digital I/O Pins (DIO): 16
Analog Input Pins (ADC): 1
UARTs: 1
SPIs: 1
I2Cs: 1
Flash Memory: 4 MB
SRAM: 64 KB
Clock Speed: 80 MHz
PCB Antenna

## Slide 12
ESP-WROOM-32
Specifications
Microprocessor: Tensilica Xtensa LX6
Maximum Operating Frequency: 240MHz
Operating Voltage: 3.3V
Analog Input Pins: 12-bit, 18 Channel
DAC Pins: 8-bit, 2 Channel
Digital I/O Pins: 39
DC Current on I/O Pins: 40 mA
DC Current on 3.3V Pin: 50 mA
SRAM: 520 KB
Communication: SPI(4), I2C(2), I2S(2), CAN, UART(3)
Wi-Fi: 802.11 b/g/n
Bluetooth: V4.2 – Supports BLE and Classic Bluetooth

## Slide 13
ECG  AD-8232
Specifications
Price: 11$
Fully integrated single-lead ECG front end
Supply current: 170 μA
Common-mode rejection ratio: 80 dB
Two or three electrode configurations
Accepts up to ±300 mV of half cell potential
Fast restore feature improves filter settling
Leads off detection: ac or dc options
Integrated right leg drive (RLD) amplifier
Single-supply operation: 2.0 V to 3.5 V

## Slide 14
ECG  AD-8232
Specifications
SDN
LO+
LO-
OUTPUT
3.3V
GND
right arm (RA)
left arm (LA)
and right leg (RL)
PINS:

## Slide 15
O2 level  MAX-30100
Specifications
Two light-emitting diodes
Two photo detectors, optimized optics and low noise simulation.
Communication modes: standard IIC protocol
Power supply: 3.3V to 5.5V
Current draw: ~600μA (during measurements)
Current draw: ~0.7μA (during standby mode)
Red LED Wavelength: 660nm
IR LED Wavelength: 880nm
Temperature Range: -40˚C to +85˚C
Temperature Accuracy: ±1˚C

## Slide 16
O2 level  MAX-30100
Specifications
VCC
GND
SCL
SDA
INT
IRD
RD
PINS:

## Slide 17
GYROSCOPE  MPU-6050
Specifications
Power supply :3-5v
Communication modes: standard IIC communications protocol
DEGREES OF FREEDOM : 6 x
Chip built-in 16bit AD converter, 16-bit data output
Acceleration range: ± 2 ± 4 ± 8 ± 16g
Pin spacing 2.54mm

## Slide 18
GYROSCOPE  MPU-6050
Specifications
VCC
GND
SCL
SDA
XCL
XDA
ADD
INT
PINS:

## Slide 19
TEMPERATURE  DS18B20
Specifications
1-Wire interface requires only one port pin for communication
Requires no external components
Power supply range is 3.0V to 5.5V
Zero standby power required
Measures temperatures from -55°C to +125°C( -67°F to +257°F)
±0.5°C accuracy from -10°C to +85°C

## Slide 20
TEMPERATURE  DS18B20
Specifications
VCC
GND
DATA
PINS:

## Slide 21
HEATING PADS
Specifications
Material: Silicon Rubber
Dimensions: 5x5cm
Voltage input: 12VDC
Power consumption: 10W

## Slide 22
CIRCUIT IMPLEMENTATION

## Slide 23
ARDUINO FLOW CHART

## Slide 24
ARDUINO SETUP
MPU-Gyroscope:
Wi-Fi connection:

## Slide 25
ARDUINO SETUP (2)
AD-8232 ECG
MAX-30100 oxygen level:

## Slide 26
OXYGEN LEVEL MAX-30100

## Slide 27
FALL DETECTION MPU-6050

## Slide 28
ECG AND HEART RATE AD-8232

## Slide 29
TEMPERATURE SENSOR DS18B20

## Slide 30
HARDWARE TESTING

## Slide 31
FALL DETECTION MPU-6050
Natural Movements
﻿-9.33 0.51 0.88 0.03 0.27 0.28 1.36 0.71 1.46 1.01 1.15
0.76 0.78 0.84 0.72 0.91 0.73 0.81 0.75 0.29 0.82 0.54
0.39 0.69 1.16 0.63 0.63 1.21 0.53 1.61 0.52 1.11 0.64
1.02 0.69 -0.21 1.47 1.29 0.33 -0.16 1.26 1.77 0.92 0.52
1.23 0.35 0.70 0.94 1.02 0.43 0.89 1.18 0.70 1.46 0.68
1.21 1.30 1.12 1.48 -0.17 1.38 -0.02 2.17 -0.11 1.31 0.47
0.58 0.06 0.34 2.36 1.79 0.69 1.60 1.17 1.11 -0.86 0.48
-0.45 1.22 0.93 0.25

## Slide 32
FALL DETECTION MPU-6050
Fall Detection with threshold [-2,+2]
0.80 0.86 2.04 Fall detected
0.96 0.05 1.27 1.33 2.11 Fall detected
0.72 0.13 23.85 Fall detected
2.39 Fall detected
0.33 0.45 0.71 2.10 Fall detected
0.62 0.72 0.42 0.83 0.56 1.14 .144 0.53 1.76 1.93
0.47 2.46 Fall detected
0.76 1.47 0.88 0.80 -2.50 Fall detected
0.99 1.28 1.65 -5.27 Fall detected
0.69 -0.62 1.60 -0.13 -2.18 Fall detected
0.10 0.16 0.41 0.42 -3.55 Fall detected 1.11 1.10 1.11 1.01 1.08 1.01 1.15 1.09 0.99 1.13
1.07 9.84 Fall detected
0.78 0.96 1.23

## Slide 33
FALL DETECTION MPU-6050
Fall Detection with threshold [-4,+4]
Fall Detection with threshold [-6,+6]
﻿0.39 0.43
0.37 0.41 0.34 0.40 0.41 0.40 0.42 0.43 0.39 0.41 -0.27
-0.47 0.43 0.90 -0.59 30.74 Fall detected
0.11 -0.40 -4.33 Fall detected
-2.07 -1.40 16.54 Fall detected
-0.48 4.90 Fall detected
-0.48 0.04 -1.62 -0.62 -0.50 4.45 Fall detected
-3.56 -1.68 -1.17 0.40 0.29
1.05 0.88 1.21 1.30 0.81 0.07 11.73 Fall detected
0.26 1.93 2.26 -0.74 0.84 1.07 -6.54 Fall detected
1.18 0.79 0.53 0.91 0.50 10.86 Fall detected
1.30 2.13 1.87 1.14 1.76 2.60 1.52 2.56 2.07 -0.22 1.92
3.99 0.96 2.31 2.71 2.81 3.85 1.12 0.85 2.77 1.30 1.36
3.77 0.70 2.08 1.15 7.59 Fall detected
1.17 0.98 1.06 1.70 2.16 0.59 0.61 0.44 9.90 Fall detected 0.06 4.93 -1.20 -0.64 19.29 Fall detected
-6.84 Fall detected
0.64

## Slide 34
1
2
3
4
AIRBAG
Fall Detection Delay
500 milliseconds
Airbag Delay
50 milliseconds
Total Delay
550 milliseconds
Equation

## Slide 35
1
2
3
HEATING PADS
Standard temperature
According to Cardinal Health, the appropriate and safe temperature range is 40-45°C.
At 9 volts
Temperature is 35.63°C
At 12 volts
Temperature is 43.94°C
Equation

## Slide 36
ECG AND HEART RATE AD-8232
1% and up to 8% error

## Slide 37
OXYGEN LEVEL MAX-30100
1% error

## Slide 38
ROOM TEMPERATURE USING MPU-6050
3
1
2
22.4°C
Room temperature is 22.4°C
22.18 °C
On MPU-6050 is 22.18 °C
1.2%
1.2% error calculated

## Slide 39
BODY TEMPERATURE USING DS18B20
2
1
3
22.31 °C
On DS18B20 is 22.31 °C
0.66%
0.66% error calculated
22.4°C
Body temperature is 22.4°C

## Slide 40
APPLICATION CHART

## Slide 41
IN DEPTH APPLICATION CHART

## Slide 42
TEMPERATURE

## Slide 43
TEMPERATURE

## Slide 44
TEMPERATURE
Arduino Side
Node.js Side

## Slide 45
TEMPERATURE
Temperature Service
Home-Page Component
Subscribe
Html Template Data Binding

## Slide 46
FALL DATA + NOTIFICATION

## Slide 47
FALL DATA QUERY

## Slide 48
ECG PLOTTING

## Slide 49
ECG SAVING

## Slide 50
ECG PLOTTING & SAVING

## Slide 51
ANGULAR PWA
Modern web technology to make websites feel more like the apps.
Use functionalities that are only for application on a website like notification.
Market of PWA will reach up to 10.77 billion dollars by 2027
Google reports a significant increase of 270% in desktop installations of PWAs from the beginning of 2021.

## Slide 52: TO INSTALL THE APP SCAN THE QR CODE

## Slide 53
RISK ASSESSMENT USING FMEA
Oxygen device malfunction
3
Software glitch
5
Heart rate device malfunction
2
Airbag malfunction
4
Heater malfunction
1

## Slide 54
TYPES OF RATING | HEATER | ECG | OXYGEN | AIRBAG | SOFTWARE
SEVERITY RATINGS | 9 | 6 | 3 | 10 | 7.5
OCCURRENCE RATINGS | 5 | 1 | 1 | 6.5 | 5.5
DETECTION RATINGS | 8 | 8 | 8 | 8 | 6
RPN | 360 | 48 | 48 | 520 | 247.5

## Slide 55
COMPONENTS | COST IN DOLLARS
ESP-8266 | $3.50
ESP-WROOM-32 | $7.77
AD-8232 + ELECTRODES | $11.00 + $6.00
MAX-30100 | $7.00
MPU-6050 | $4.00
DS18B20 | $2.00
HEATING PADS | $6.00 * 2
JACKET | $15.00
POWER BANK | $20.00
ADDITIONAL MATERIAL (BREADBOARD, WIRES ETC..) | $20.00
TOTAL COST | $108.27

## Slide 56
WORK BREAKDOWN
Project Initiation
1.1. Collect all items
1.2. Test all collected items
Tangible Implementation
3.1. Design jacket
3.2. Add all components
Hardware Development
2.1 Hardware connections
2.2 Hardware coding
Testing
Application Development
4.1.1. Front-end Development
4.1.2 Back-end Development
4.2. Deployment
1.
2.
3.
4.
5.

## Slide 57
ACTIVITY | JUL | AUG | SEP | OCT | NOV
GET ALL COMPONENTS NEEDED | ELIE & ATIEH | ELIE & ATIEH |  |  | 
PROGRAM THE HEART RATE |  |  | ELIE |  | 
PROGRAM THE OXYGEN SENSOR |  |  | ATIEH |  | 
PROGRAM THE TEMPERATURE SENSOR |  |  | ELIE |  | 
PROGRAM FALL SENSOR |  |  | ATIEH |  | 
DESIGN JACKET |  |  |  | ELIE & ATIEH | 
ADD ALL COMPONENTS |  |  |  | ELIE & ATIEH | 
CREATE THE FRONT-END |  |  |  | ELIE & ATIEH | 
CREATE THE BACK-END |  |  |  | ELIE & ATIEH | 
DEPLOY ON SERVER |  |  |  |  | ELIE
TEST ALL COMPONENTS |  |  |  |  | ELIE& ATIEH

## Slide 58
THANK YOU!
KEEP YOUR ELDERLY SAFE